## Slide 1: Memory Bandwidth Management for Enhanced Throughput and Security in GPUs
Adwait Jog
Assistant Professor of Computer Science
College of William & Mary
http://adwaitjog.github.io/

## Slide 2: William & Mary
Second oldest-institution of higher education in the US
Located in Williamsburg, VA. Recently hosted ASPLOS.
I am affiliated with Computer Science Department
  Graduate Program (~65-70 Ph.D. students)
  25 Faculty Members
Many graduated Ph.D. students have successfully established careers in academia & industry.

## Slide 3: Insight Computer Architecture Lab
More details: http://insight-archlab.github.io/
Gurunath Kadam
(Ph.D. student)
Mohamed Ibrahim (Ph.D. Student)
Fan Luo
(MS student, graduated)
Hongyuan Liu
(Ph.D. student)
Haonan Wang
(Ph.D. student)
Major Funding Source:
National Science Foundation
Adwait Jog
(Faculty)
NSF CAREER (’18--)
NSF CORE (’17--)
NSF CRII (’17--)

## Slide 4: Current Research Interests
We are computer architects
  Architecting Graphics Processing Units (GPUs) and other accelerators of the future
  GPU Security and Reliability
  Non-traditional architectures (e.g., Automata Processors)

## Slide 5: Why GPUs?
Astronomy
Medical
Imaging
Audio
Processing
Machine
Learning
Physics
Simulation
Games
Image Processing
Financial Computing
Genomics
Data-Level Parallelism
Large
Data Sets

## Slide 6: Why GPUs?
Large Number of Cores
GPU
General-purpose Computing
on GPUs (GPGPUs)
Applications

## Slide 7: How Acceleration Works
Fewer Cores
Optimized for Latency
Great for Sequential Code
Large Number of Cores
Optimized for Throughput
Great for
Parallel Code
Application Code
Sequential Code
Parallel Code
Sequential Code
Many supercomputers
in the green500 list employ accelerators.
Accelerator
(e.g., GPU)
Notes: Do not use the word “offload”

## Slide 8: SUMMIT Super Computer
Multiple Volta GPUs
NVLink
HBM + DDR4
https://www.olcf.ornl.gov/olcf-resources/compute-systems/summit/

## Slide 9: GPU Scaling Trends
GTX 980
(Maxwell)
2048
CUDA
Cores
(224
GB/sec)
GP 100
(Pascal)
3584
CUDA
Cores
(720
GB/sec)
GV 100
(Volta)
5120
CUDA
Cores
(900
GB/sec)
GTX 680
(Kepler)
1536
CUDA
Cores
(192
GB/sec)
GTX 275
(Tesla)
240
CUDA
Cores
(127
GB/sec)
GTX 480
(Fermi)
448
CUDA
Cores
(139
GB/sec)
Notes: As we know GPU are scaling both in terms of number of CUDA cores as well peak DRAM
Bandwidth. For example, the latest NVIDIA GPU GTX 980 has more than 2000 cores.
Given such powerful GPUs, the question is -- Are we “still” using them efficiently?

## Slide 10: Making Good Use of Resources (1)
Deep Learning and Artificial Intelligence
Credit: NVIDIA AI

## Slide 11: Making Good Use of Resources (2)
Multiple CPUs send requests to GPUs
  Multiple requests from users consolidated in the cloud data center (e.g., NVIDIA GRID)
CPU-1
CPU-2
CPU-3
CPU-N

## Slide 12: Memory Bandwidth
One of the major resources in GPUs is memory bandwidth. We need to manage it carefully.
[Performance and Fairness] Current bandwidth optimizations can lead to sub-optimal performance and fairness for multi-application execution.
[Performance and Security] Current bandwidth optimizations (e.g., coalescing) can lead to security vulnerabilities.
Our focus is on developing new bandwidth optimization techniques to improve performance, fairness, and security.

## Slide 13: Outline
Memory Bandwidth Management for Performance and Fairness
  Efficient and Fair Multi-programming in GPUs via Effective Bandwidth Management, HPCA’18
  Focuses on Performance / Fairness Trade-offs
Memory Bandwidth Management for Performance and Security
  RCoal: Mitigating GPU Timing Attack via Subwarp-based Randomized Coalescing Techniques, HPCA 2018
  Focuses on Performance / Security Trade-offs

## Slide 14: Efficient and Fair Multi-programming in GPUs via Effective Bandwidth Management
Haonan Wang, Fan Luo, Mohamed Ibrahim
(College of William & Mary), Onur Kayiran (AMD),
Adwait Jog (College of William & Mary)
Notes: Hi, my name is Mohamed Assem Ibrahim. Today, I will present our work “Efficient and Fair Multi-programming in GPUs via Effective Bandwidth Management”. This work was jointly performed with my advisor and colleagues at The Collage of William and Mary and our collaborators at AMD.
+++++++++++++++++++++++++++++++++++++
Don’t use
-----------
OK
Right?
Sort of

## Slide 15: Executive Summary
Goal: Address the BW interference problem via Thread-level Parallelism (TLP) modulation
Contributions:
  Observe that prior single-application TLP modulation schemes do not provide optimal throughput (WS) and fairness (FI) in a multi-application environment
  Propose a new metric Effective Bandwidth (EB) to quantify the effects of TLP modulation
  Design new application-aware TLP management techniques (PBS) for a better throughput/fairness
  PBS improves Throughput (up to 20%) and Fairness (up to 2x) over using single-application TLP modulation schemes in a multi-application environment
Notes: As a quick overview of our work, we investigate multi-application execution on GPUs. It can increase the resource utilization and overall throughput. Also, it enables sharing GPUs in the cloud. However, it is difficult to efficiently manage the shared BW resources in such environment.
Our goal is to address the BW interference problem using Thread-level Parallelism modulation.
Our contribution is three-fold. First, we studied the prior single-application TLP modulation schemes in a multi-application environment, and found that they don’t provide optimal system throughput and fairness. Second, we propose Effective Bandwidth (EB), a new metric to understand performance in single- and multi-application execution context. Finally, we develop a new application-aware scheme, PBS, that utilizes EB to achieve better throughput and fairness.
PBS improves system throughput up to 20% and achieves up to 2x fairness compared to using single-application TLP modulation schemes in a multi-application environment.
+++++++++++++++++++++++++++++++++++++
Onur: EB is not only for quantifying the effects of TLP modulation. Don't downplay its importance. It is for understanding performance in general, but it is specifically more useful in the context of multi-application execution.
PBS is within 3% and 6% of optWS and optFI
Our proposed pattern-based TLP management mechanisms improve the system throughput and fairness by 20% and 2x, respectively, over a baseline where each application executes with a TLP configuration that provides the best performance when it executes alone.

## Slide 16: Managing TLP for Single-Application
Thread-level Parallelism
TLP
Number of Wavefronts/Warps
Cache Hit/Miss Behavior
DRAM Bandwidth Behavior
Change
Cache
DRAM
Notes: TLP can be used as a knob to manage resources utilization. We start by showing how TLP modulation can be used in a single-application scenario.
As we see in the figure, TLP directly affects the number of wavefronts running, which affects the number of concurrent threads.
As a result, it affects the cache behavior in terms of hit and miss requests.
TLP also affect the DRAM BW behavior.
Now if we increase the TLP value, then we can see a change in both the cache and BW behavior.
+++++++++++++++++++++++++++++++++++++
Onur: The blue arrows in DRAM are not very visible. Maybe red will be better. Or you can make them wider.
Show the DRAM utilization in a better/clear way
Number of Warps = Number of Wavefronts
In particular, the techniques that find the optimal thread-level parallelism (TLP) of a GPGPU application were found to be very effective in improving the GPU performance both for cache and memory-intensive applications [30], [50]. The key idea behind these techniques is to exploit the observation that executing a GPGPU application with the maximum possible TLP does not necessarily result in the highest performance. This is because as the number of concurrently executing threads increases, the contention for cache space and memory bandwidth also increases, which can lead to sub-optimal performance. Therefore, many of the TLP management techniques proposed to limit the TLP via limiting the number of concurrently executing warps (or wavefronts2) to a particular value.

## Slide 17: Managing TLP for Single-Application
bestTLP | the best-performing TLP configuration
maxTLP | the maximum possible value of TLP
A single application is executed with
Chart: TLP
| 1.0 | 2.0 | 4.0 | 8.0 | 12.0 | 16.0 | 20.0 | 24.0
IPC | 0.71861 | 0.95485 | 1 | 0.95529 | 0.92737 | 0.91988 | 0.92194 | 0.92386
bestTLP
maxTLP
Notes: For example, this figure shows how changing the TLP can affect the performance of an application. On the x-axis is the different TLP values, and on the y-axis in the normalized IPC.
We first identify two points. “bestTLP” is the TLP configuration with the best IPC, and “maxTLP” is the configuration with the maximum possible TLP value.
We point out two observations. First, using “maxTLP” doesn’t lead to the best IPC. This is because as the number of concurrently executing threads increases, the contention for cache and memory bandwidth also increases, which may lead to sub-optimal performance. Second, as the TLP value increases, the IPC increases till we reach “bestTLP”. After that IPC drops. This is because the increase in BW utilization cannot compensate the increase in cache miss rate.
+++++++++++++++++++++++++++++++++++++
Application = CUDA-BFS2

## Slide 18: Challenges of Managing TLP for Multi-Application
++bestTLP | their own respective bestTLP configurations
++maxTLP | their own respective maxTLP configurations
optWS/optFI | their own TLP configurations such that WS/FI is maximized
Two or more applications are executed concurrently with
Chart: Normalized WS
| ++maxTLP | optWS
 | 0.92009 | 1.2957
Chart: Normalized FI
| ++maxTLP | optFI
 | 0.9504 | 2.0352
++bestTLP
++bestTLP
Why?
Notes: To understand the scope of TLP modulation in the context of two-application execution, we analyzed three different scenarios.
First, both applications executes with their respective “bestTLP” referred to as “++bestTLP”. Second, both applications executes with their respective “maxTLP” referred to as ”++maxTLP”. Finally, both applications executes with TLP configuration such that system throughput or fairness is maximized.
From the figure, we can see that there is a significant gap in WS between optWS and ++bestTLP/++maxTLP combinations running BFS2_FFT workload. The same applies for fairness (FI).
Thus, blindly using the single-application TLP modulation schemes in the context of multi-application execution is sub-optimal. But why?
+++++++++++++++++++++++++++++++++++++
Workload = BFS2_FFT

## Slide 19: Why?
Some applications consume less/more resources compared to co-running application(s)
  Difficult management of BW resources in GPUs
Application#1
TLP
Application#2
TLP
L2 Cache
DRAM
How to manage the application interference in the shared caches and main memory to achieve the maximum benefits of multi-application execution?
BW Interference Problem
Notes: This figure shows two co-running applications. Each is given half of the shared resources. We can see that application#1 is consuming its half of the resources as shown in blue, while application#2 is not as shown in green.
This underutilization of resources is because applications have different resources requirement. That is what makes managing the shared BW resources a challenging problem.
Specifically, the BW interference problem is how to manage the applications interference in the shared resources to achieve maximum benefits from multi-application execution.
+++++++++++++++++++++++++++++++++++++
Onur: Why is the negative point about "being unfair"? It might cause people to think about "fairness".
Should we explicitly mention that such configurations consider local information only?

## Slide 20: Proposal
Contribution
Design new TLP management techniques that can bridge the gap in System Throughput and Fairness
Optimizing performance by considering core-level metrics locally
Application-aware TLP management that make good and judicious use of all the shared resources available
Goal
Address the BW interference problem in multi-application execution environment
Notes: In this work, we address the BW interference problem in a multi-application environment.
We develop new TLP management schemes to bridge the gap in system throughput and fairness.
We don’t rely ONLY on local per-core metrics.
But we consider the shared resources as well.
+++++++++++++++++++++++++++++++++++++
TLP technique focusing on BW interference problem.
Although previously proposed TLP modulation techniques (e.g., DynCTA and CCWS) have been shown to be effective in optimizing TLP for single-application execution scenarios, they rely only on different kinds of per-core heuristics (e.g., latency tolerance, IPC, cache/memory contention) and do not consider the shared resource consumption of co-scheduled applications. In other words, each application under such TLP configurations (including bestTLP) attempts to maximize its own effective bandwidth, ultimately taking disproportionate amount of shared resources. This causes too much contention in caches and memory, ultimately hampering the system-wide metrics such as system throughput and fairness.

## Slide 21: Effective Bandwidth: A New Metric to Measure Resource Consumption
Core
L1
L2
DRAM
A
B
C
An application-level utility metric defined as the ratio of attained DRAM bandwidth to the cache miss rate (based on current level of hierarchy)
Notes: Effective Bandwidth, EB, is an application-level utility metric, defined as the ratio between the DRAM bandwidth and the cache miss rate based on level of hierarchy under consideration.
For example, in this figure, EB @ point A is the same as the DRAM BW. However, @ point B, EB is the ratio between DRAM BW and L2 miss rate. Finally, @ point C, @ the core, EB is ratio between DRAM BW and the combined miss rate. CMR is the product of L1 and L2 cache miss rates.
+++++++++++++++++++++++++++++++++++++
- Metric concerning BW as BW interference is the main problem.

## Slide 22: Effective Bandwidth: A New Metric to Measure Resource Consumption
Measures how well the DRAM bandwidth is utilized
Considers the usefulness of the caches in amplifying the performance
Chart: TLP
| 1.0 | 2.0 | 4.0 | 8.0 | 12.0 | 16.0 | 20.0 | 24.0
Goodness | 0.72103 | 0.95087 | 1 | 0.95275 | 0.93598 | 0.92714 | 0.92781 | 0.9257
Chart: TLP
| 1.0 | 2.0 | 4.0 | 8.0 | 12.0 | 16.0 | 20.0 | 24.0
L2MRxL1MR | 0.98239 | 1.0005 | 1 | 1.3667 | 2.5523 | 2.8313 | 2.8629 | 2.922
Chart: TLP
| 1.0 | 2.0 | 4.0 | 8.0 | 12.0 | 16.0 | 20.0 | 24.0
BW | 0.70833 | 0.95139 | 1 | 1.3021 | 2.3889 | 2.625 | 2.6562 | 2.7049
Chart: TLP
| 1.0 | 2.0 | 4.0 | 8.0 | 12.0 | 16.0 | 20.0 | 24.0
IPC | 0.71861 | 0.95485 | 1 | 0.95529 | 0.92737 | 0.91988 | 0.92194 | 0.92386
Why EB?
Combined Miss Rate (CMR)
Notes: But why EB?
EB measures both the DRAM BW utilization and the usefulness of the caches in amplifying the performance. Let us look at EB benefit analytically and experimentally.
Analytically, performance, in terms of IPC, is the ratio between DRAM BW and the product of rm (which is related to the compute to memory ratio) and the combined cache miss rate.
Then, IPC is directly proportional to EB.
This can be shown by monitoring the IPC and the EB. We can see that both IPC and EB follow the same trend when TLP changes. Also, we can see that up to TLP=4 both IPC and EB increases as the increase in BW is more that the increase in CMR. However, after TLP=4, EB drops as the increase in BW is not enough to compensate the increase in CMR. IPC also drops as the contention for cache and memory bandwidth increases.
This shows that EB is a good metric to optimize for performance in a single-application scenario, but what about multi-application?
+++++++++++++++++++++++++++++++++++++
Application = CUDA-BFS2

## Slide 23: EB in Multi-Application Environment
Chart: Workloads
Example: For BLK and BFS2 workload, IPC ratio is 25 but EB ratio is 2

## Slide 24: EB in Multi-Application Environment
Slowdown | SD | 
Weighted Speedup | WS | 
Fairness Index | FI | 
Slowdown | SD | 
Weighted Speedup | WS | 
Fairness Index | FI | 
Effective Bandwidth | EB | 
Weighted Speedup |  | 
Fairness Index |  | 
Effective Bandwidth | EB | 
Weighted Speedup |  | 
Fairness Index |  | 
EB-based Metrics
SD-based Metrics
Challenge?
A TLP management scheme that optimizes for EB-based metrics is useful in improving system throughput and fairness
Easier to calculate in shared environment
Details in paper
Notes: However, a management scheme that optimizes for EB-based metrics is useful in improving system throughput and fairness.
Thus, we introduce our version of the SD-based metrics for system throughput and fairness and utilize EB instead of slowdowns. For example, EB-WS is the sum of EBs instead of using the sum of slowdowns. Another, crucial factor here is that EB-based metrics don’t incorporate any alone-execution information. This makes EB-based metrics easier to calculate in a multi-application environment.
But what is the challenge in using EB?
+++++++++++++++++++++++++++++++++++++
Mention the alone information in SD-based metrics vs. EB-based metrics.
EB-WS (EB-based) metric does not incorporate any alone-application information making it easier to calculate directly in a multi-application environment.
Note: In the latter case, each application uses the value of EB when it executes alone and uses bestTLP. As we cannot get this information unless we halt the other co-running applications, we approximate it by executing the co-runners with the least amount of TLP (i.e., 1) so that they induce the least amount of interference possible.

## Slide 25: Challenge? Search Space
Finding the TLP combination is difficult
  Huge search space
    Assume applications with
  Sampling period to collect and
Solution?
Notes: Finding the optimal TLP configuration is difficult. This is due to the huge search space. For example, using n co-running applications, while selecting from 8 TLP values per application, leads to 8^n search space.
Add the sampling period required, per configuration, to collect BW and CMR, this shows how bad a naïve searching technique can fail.
So, what is the solution?
+++++++++++++++++++++++++++++++++++++
We need an intelligent way to find the required TLP

## Slide 26: Pattern-Based Searching (PBS)
To reach optimal system throughput
Choose a TLP configuration that does not underutilize the shared resources
Guideline-1
To avoid sharp drops in one (or all) applications’ EB, hence inferior throughput and fairness
Choose a TLP configuration which would not overwhelm the DRAM BW
Guideline-2
Pattern?
Notes: We start by emphasizing two guidelines. First, EB-based metrics are sub-optimal if a TLP configuration leads to resources underutilization. Thus, to reach optimal system throughput, choose a TLP configuration that does not underutilize the shared resources.
Similarly, we should choose a TLP configuration that does not overwhelm the shared resources. This is because EB-based metrics start to drop when the increase in BW can no longer compensate the increase in CMR.
Now, we define the pattern used in the searching scheme.
+++++++++++++++++++++++++++++++++++++
Total EB can be sub-optimal when a particular TLP configuration leads to under-utilization of resources (DRAM and BW)
Guideline-1. The EB-based metrics are sub-optimal when a particular TLP combination leads to under-utilization of resources (e.g., DRAM bandwidth). Therefore, for obtaining the optimal system throughput, it is important to choose a TLP combination that does not under-utilize the shared resources.
EB of an application starts to drop only when its BW can no longer compensate for the increase in its CMR
Guideline-2. When increasing an application’s TLP level, its EB starts to drop only when the increase in its BW can no longer compensate for the increase in its CMR (i.e., EB at its inflection point). Therefore, it is important to choose a TLP combination that would not overwhelm resources as it is likely to cause sharp drops in one or all applications’ EB, leading to inferior system throughput and fairness.

## Slide 27: Pattern-Based Searching (PBS)
Pattern
Chart: TLP-BLK
| 1.0 | 2.0 | 4.0 | 8.0 | 12.0 | 16.0 | 20.0 | 24.0
TLP-TRD-1 | 0.56263 | 0.73335 | 0.76312 | 0.80352 | 0.81514 | 0.81706 | 0.81135 | 0.81441
TLP-TRD-2 | 0.876 | 0.93872 | 0.78769 | 0.82326 | 0.83493 | 0.83485 | 0.83096 | 0.83725
TLP-TRD-4 | 1.1798 | 1.3101 | 0.89652 | 0.86354 | 0.87899 | 0.87656 | 0.87115 | 0.8745
TLP-TRD-8 | 1.336 | 1.4426 | 0.97079 | 0.90918 | 0.91323 | 0.90315 | 0.91039 | 0.90636
TLP-TRD-12 | 1.3539 | 1.4359 | 0.99652 | 0.89829 | 0.91479 | 0.90836 | 0.90979 | 0.9088
TLP-TRD-16 | 1.302 | 1.4188 | 0.98828 | 0.90074 | 0.91495 | 0.91635 | 0.91764 | 0.89225
TLP-TRD-20 | 1.2879 | 1.3872 | 0.96998 | 0.8965 | 0.91025 | 0.91524 | 0.89779 | 0.91071
TLP-TRD-24 | 1.2858 | 1.3936 | 0.97174 | 0.89756 | 0.91294 | 0.91567 | 0.89788 | 0.90952
Significant drop in EB-based metric happens at a fixed TLP of a particular application, when the resources in the system are sufficiently utilized, regardless of TLP of other co-running application(s)
Notes: The figure show the execution of BLK_TRD workload, with EB-WS on the y-axis. We vary the TLP values of BLK on the x-axis, and show the different TLP values of TRD as colored/dashed lines.
The pattern:
- is a significant drop in the EB-based metric
- that happens at a fixed TLP of a particular application
- when the resources are sufficiently utilized
- regardless of the TLP of the other co-running application
For example, we see that EB-WS drops @ TLP-BLK = 2 regardless the TLP value of TRD. We refer to this as the pattern for BLK.
+++++++++++++++++++++++++++++++++++++
at the DRAM BW saturation point? How to show that?
Significant drop in EB happens at a fixed TLP of a particular application at the DRAM BW saturation point (regardless of TLP of other co-running applications)

## Slide 28: PBS – High-level Searching Process
Tune the co-running application TLP to optimize the EB-based metric
Reducing the search space from (Exponential) to (Linear)
2- Tune the Co-running Application(s)
Sequentially check each application for the pattern while maintaining full resource utilization
1- Find the Critical Application
The sharpest drop in EB-based metrics is attributed to the critical application
Notes: Now, we give a high-level overview for our searching scheme.
First, we search for what we refer to as the critical application. We do that by sequentially checking each of the co-running applications for the pattern.
The application with the sharpest drop in the EB-based metric is the critical application.
Second, we fix the TLP of the critical application @ its inflection point and sequentially tune the co-running application(s) to optimize the EB-based metric.
This process reduces the exponential search space to a linear one.
+++++++++++++++++++++++++++++++++++++

## Slide 29: Evaluation Methodology
Evaluated on MAFIA
  A GPGPU-Sim based framework that can execute two or more applications concurrently
Baseline Configuration
  30 SMs, 32-SIMT Lanes, 32 Threads/Wavefront, 48 Wavefronts
  16KB L1 (4-way, 128B Cache Block) + 32KB Shared Memory per SM
  256KB L2 (16-way, 128B Cache Block) per Memory Partition
  6 Memory Partitions
  1 Crossbar/Direction
Workloads
  26 Single Applications
    From Rodinia, Parboil, CUDA SDK, and SHOC
  50 Two-application Workloads
  20 Three-application Workloads
Notes: We evaluate PBS on MAFIA, a GPGPU-Sim based framework that executes two (or more) applications concurrently.
We use 30 cores equally divided between the co-running applications. For example, in case of two-application scenario, each application is statically assigned 15 cores. However, the L2 cache and DRAM BW are shared.
We use 26 applications from different benchmarks suites to evaluate 50 two-application workloads, and 20 three-application workloads.
+++++++++++++++++++++++++++++++++++++
Extended GPGPU-Sim v3.x (Simulator) and developed GPU concurrent application framework (GCA) to enable multi-programming in GPUs.
The memory performance model is validated across several GPGPU workloads on an NVIDIA K20m GPU.
To understand how these applications interfere in the shared memory system, each application is mapped to an exclusive set of cores and allowed to use resources beyond the cores (e.g., L2, DRAM). We allocate an equal number of cores to each concurrently executing application. Sensitivity to different core and L2 cache partitioning techniques is discussed later.

## Slide 30: Evaluation – Throughput
Chart: Normalized WS (to ++bestTLP)
| 3DS_TRD | BFS2_FFT | BLK_BFS2 | BLK_TRD | FFT_TRD | FWT_TRD | JPEG_CFD | JPEG_LIB | JPEG_LUH | SCP_TRD | Gmean
++DynCTA | 0.98243 | 1.0386 | 1.1491 | 1.0455 | 1.1027 | 1.1216 | 1.1121 | 1.1046 | 0.96442 | 1.2423 | 1.0761
Mod+Bypass | 1.05 | 1.15 | 1.19 | 1.1 | 1.1 | 1.13 | 1.11 | 1.13 | 1.08 | 1.25 | 1.09
PBS-WS | 1.2438 | 1.3027 | 1.249 | 1.2956 | 1.1151 | 0.89722 | 1.1447 | 1.2929 | 1.2925 | 1.2613 | 1.1968
optWS | 1.2579 | 1.2957 | 1.214 | 1.291 | 1.2063 | 1.1624 | 1.1613 | 1.1903 | 1.2016 | 1.2887 | 1.2264
++DynCTA
Mod+Bypass
optWS
++bestTLP
+19.6%
+11.2%
+9.7%
-3%
[Kayiran+, PACT2013]
[Li+, DATE2016]
Notes: We start with system throughput. This figure shows the normalized WS on the y-axis normalized to ++bestTLP.
Our scheme, PBS-WS, achieves 19.6% improvement over ++bestTLP.
Also, PBS-WS achieves 11.2% improvement over a scheme that uses DynCTA, which is a single-application TLP modulation scheme, to determine the TLP for each co-running application.
PBS-WS achieves 9.7% improvement over a recently proposed TLP management mechanism Mod+Bypass, that use CTA modulation and cache bypassing to enhance the system throughput in multi-application scenario.
Finally, our scheme is within 3% from the optimal WS.
+++++++++++++++++++++++++++++++++++++
This is because in “++bestTLP” or “++maxTLP” scenarios, each application assumes that no other application is co-scheduled. That leads to high cache and memory contention.
Explain FWT_TRD?
Impact of our schemes on Weighted Speedup. Results are normalized to ++bestTLP.
We compare the PBS mechanisms against the recently proposed TLP management mechanism Mod+Bypass for multi-application scenario. They use both CTA modulation and cache bypassing mechanism to enhance the system throughput.

## Slide 31: Evaluation – Fairness
Chart: Normalized FI (to ++bestTLP)
| 3DS_TRD | BFS2_FFT | BLK_BFS2 | BLK_TRD | FFT_TRD | FWT_TRD | JPEG_CFD | JPEG_LIB | JPEG_LUH | SCP_TRD | Gmean
++DynCTA | 1.5139 | 1.39 | 1.602 | 1.1077 | 1.2215 | 1.1693 | 0.81022 | 0.88183 | 0.84869 | 1.5409 | 1.1247
Mod+Bypass | 1.78 | 1.51 | 1.74 | 1.33 | 1.48 | 1.34 | 1.03 | 1.24 | 1.13 | 1.96 | 1.4265
PBS-FI | 2.1352 | 2.1278 | 2.64 | 3.3234 | 3.1388 | 2.0407 | 1.4371 | 2.3395 | 2.224 | 2.2401 | 2.0596
optFI | 2.0075 | 2.0352 | 2.5756 | 2.9809 | 2.9071 | 2.375 | 2.2636 | 2.2879 | 2.1158 | 2.1967 | 2.1751
++DynCTA
Mod+Bypass
optFI
++bestTLP
2X
+83.1%
+44.3%
-6%
[Kayiran+, PACT2013]
[Li+, DATE2016]
Notes: We move to fairness. This figure shows the normalized fairness index (FI) on the y-axis normalized to ++bestTLP.
Our scheme, PBS-FI, improves fairness by 2x compared to ++bestTLP.
Also, PBS-FI achieves 83.1% improvement over a scheme that uses DynCTA.
PBS-FI achieves 44.3% improvement over using Mod+Bypass.
Finally, our scheme is within 6% from the optimal FI.
+++++++++++++++++++++++++++++++++++++
PBS-FI is better than optFI?
Impact of our schemes on Fairness. Results are normalized to ++bestTLP.

## Slide 32: Conclusion
Observe an ample scope for TLP management techniques to improve WS and FI in GPUs running multiple applications
Propose a new metric EB to quantify the effects of TLP modulation
Design PBS, EB-based application-aware TLP management techniques for a better WS/FI in a multi-application environment
  PBS is within 3% and 6% of optWS and optFI
Notes: To conclude, we observed a large scope a TLP management scheme to improve system throughput and fairness in a multi-application environment.
We proposed a new metric called Effective Bandwidth to model the performance in a single- and multi-application scenarios.
Also, we designed PBS, EB-based application aware TLP management schemes to enhance WS and fairness. Our results are within 3% and 6% of optimal WS and fairness.
+++++++++++++++++++++++++++++++++++++
Should I add “PBS improves WS (up to 20%) and FI (up to 2x)”?

## Slide 33: Outline
Memory Bandwidth Management for Performance and Fairness
  Efficient and Fair Multi-programming in GPUs via Effective Bandwidth Management, HPCA’18
  Focuses on Performance / Fairness Trade-offs
Memory Bandwidth Management for Performance and Security
  RCoal: Mitigating GPU Timing Attack via Subwarp-based Randomized Coalescing Techniques, HPCA 2018
  Focuses on Performance / Security Trade-offs

## Slide 34: RCoal: Mitigating GPU Timing Attack via Subwarp-based Randomized Coalescing Techniques
Gurunath Kadam (College of William & Mary)
Danfeng Zhang (Penn State University)
Adwait Jog (College of William & Mary)

## Slide 35: Security Concerns
GPUs may be accelerating applications that are using user-sensitive data (e.g., genomics, financial)
GPUs may be accelerating cryptographic applications (e.g., AES, RSA etc.) and authentication algorithms on-behalf of CPUs
Given the popularity of GPUs, It is imperative to keep GPUs secure against a variety of side-channel attacks and other security vulnerabilities.

## Slide 36: Security Attacks
User’s web activity on GPU can be tracked by the malicious attacker who is co-located on the same card [Oakland 2014]
AES private keys can be recovered by correlation timing attacks [HPCA 2016]
More severe attacks on GPUs? [Oakland’18]
  Spectre/Meltdown like attacks for GPUs?

## Slide 37: Correlation Timing Attacks
Plaintexts | Ciphertexts | Time duration
Plaintext # 1
time1
timestart
- timestop = time1
Plaintext # 2
time2
Plaintext # 3
time3
…
…
Attacker
Server
Ciphertext # 1
Ciphertext # 2
Ciphertext # 3
…
K1 , K2 , … ,
Ki
, …
Key guesses
Correct Key
Correct Key??
Notes: This should be a general timing attack description

## Slide 38: Correlation Timing Attacks
GPU
Are GPUs vulnerable to Correlation Timing Attacks?
GPUs implement SIMD paradigm
Fast and energy efficient computations
Accelerate the cryptographic algorithms
Notes: Highlight the GPU – Make bigger put block
Highlight the importance of GPU in words

## Slide 39: Summary of our HPCA’18 work
Prior Work: Correlation Timing Attacks on GPUs ([Jiang/Fei/Kaeli, HPCA’16])
  Coalesced memory accesses and execution time are correlated.
  AES key value affects the coalesced accesses.
  Coalescing procedure is deterministic and known to the attacker.
  Attacker can recover AES key by calculating coalesced accesses and correlating it with the execution time.
Our Contribution: Randomizing the Coalescing Mechanism (RCoal)
  Goal: Make the calculation of coalesced accesses harder for the attacker.
  Our proposal: Three novel coalescing mechanisms that randomize the size, number, and thread-elements of a sub-warp.
  Results: RCoal improves security by 24- to 961- times at a modest performance loss of 5 to 28%.
Notes: In to two slides – show successful and unsuccessful correlation plots
  Last round memory accesses can be determined using AES key.
  Memory accesses are coalesced together deterministically by GPUs and hence can be calculated correctly by an attacker.
  Number of coalesced memory accesses correlates with the execution time.

## Slide 40: Memory Access Coalescing in GPUs
Streaming Multiprocessor
Warp pool
Warp
Thread # 1
Thread # 32
. . .
Warp Scheduler
LD/ST Unit
Global Memory
Coalescing Unit

## Slide 41: Memory Access Coalescing in GPUs
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
0x00
0x04
0x07
0x09
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
WARP
tid = thread id
Block Address # 0
Block Address # 1
Block Address # 1
Block Address # 2

## Slide 42: Memory Access Coalescing in GPUs
Coalescing Unit
0x00
0x01
0x02
0x03
0x08
0x09
0x0A
0x0B
0x00
0x04
0x07
0x09
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
WARP
tid = thread id
Block Address # 0
Block Address # 1
Block Address # 2

## Slide 43: AES implementation on GPU
Symmetric Encryption with 128-bit key and 10 rounds.
S-box implementation involves table lookups.
[Jiang/Fei/Kaeli, HPCA’16] demonstrated that the last round is vulnerable.

## Slide 44: Last Round of AES on GPU

## Slide 45: Last Round of AES on GPU
LINE # 1
LINE # 2
LINE # 32
…
…
ti1
ti2
ti32
.
.
.
Input text
to Last Round
…
…
.
.
.
Thread # 1
Thread # 2
.
.
.
Thread # 32
.
.
.
T4[ti2]
T4[ti1]
T4[ti32]
Request # 1
Request # 2
.
.
.
Request # 32
Coalescing
Unit
.
.
.
⊕ kj
⊕ kj
⊕ kj
Replies # 1
Replies # 2
.
.
.
Replies # 32
cj1
cj2
cj32
.
.
.
Ciphertext

## Slide 46: Correlation Timing Attack on GPU
Goal of the attack: Recover the AES Key (byte-by-byte)
Last Round of AES is vulnerable
Last Round is invertible
Memory access
of thread tid
How an attacker can calculate the number of coalesced accesses?
Notes: After the goal, Attack model – using figure slide 2. What is available to the attacker – ciphertext, execution time and AES Tables.

## Slide 47: Attacker calculates the # of coalesced accesses
…
…
cj1
cj2
cj32
.
.
.
Ciphertext
.
.
.
⊕ kjm
⊕ kjm
⊕ kjm
.
.
.
.
.
.
T4-1[cj2⊕kjm]
T4-1[cj1⊕kjm]
T4-1[cj32⊕kjm]
ti1,m
ti2,m
ti32,m
.
.
.
Guessed Table
Lookup Indices
.
.
.
.
.
.
Coalesced Accesses
(Ajm,n)
Correct value of key byte?

## Slide 48: Coalesced Accesses and Execution Time
Associate the number of coalesced accesses with execution time
Notes: Say on our set-up

## Slide 49: Finding the Correct Key Value
Attacker encrypts ‘N’ number of plaintexts over server
  Records Ciphertext and Execution time
Aj0,1, Aj0,2, . . . . , Aj0,N
E1,E2,...,EN
Key Guess 0
Key Guess 1
Key
Guess 255
Corrj0
Corrj1
Corrj255
Key
Guess α
Corrjα
Maximum Correlation
Aj1,1, Aj1,2, . . . . , Aj1,N
Ajα,1, Ajα,2, . . . . , Ajα,N
Aj255,1, Aj255,2, . . . . ,Aj255,N
.
.
.
.
.
.
.
.
.
.
.
.
Recorded
Execution Time
Correct
Key Byte
# of Coalesced Accesses
Correlations
Notes: Eliminate the slide transition

## Slide 50: Simulating Timing Attack on our Set-up
Correct guess
Incorrect guesses
Why is Correlation Timing Attack possible?
The baseline attack leverages the deterministic nature of the coalescing mechanism
AES key value affects the coalesced accesses
# coalesced accesses affects the execution time
How to mitigate Correlation Timing Attacks on GPU?
Answer: By making it harder for the attacker to correctly calculate the number of coalesced accesses
Notes: TODO: Coalescing good for performance and bad for security

## Slide 51: Naïve Solution
Disable coalescing altogether?
  Correlation drops to ~0
  Correct key byte is indistinguishable
Up to 178% performance degradation
  Degradation increases with plaintext size
Correct guess
Naïve solution is Good for Security, Bad for Performance
Offers no tradeoff
Targets the deterministic nature of the coalescing mechanism
  Fixed number of subwarps
  Fixed sizes of subwarp
  Deterministic mapping of the thread elements to subwarps
RCoal to mitigate the correlation timing
attacks

## Slide 52: RCoal: Fixed Sized Subwarp (FSS)
Coalescing Unit
0x00
0x01
0x02
0x03
0x08
0x09
0x0A
0x0B
DEFAULT: number of subwarps = 1
0x00
sid = 0
0x04
0x07
0x09
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
Coalescing Unit
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
FSS: number of subwarps = 2
0x00
sid = 0
0x04
0x07
sid = 1
0x09
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
Notes: Fixed Size Subwarp eliminates the fixed number of subwarps based determinism.

## Slide 53: FSS Security against Baseline Attack
Correlation between the number of coalesced accesses and the execution time drops
Correct key byte is harder to find
Improved security

## Slide 54: FSS Performance
Memory accesses increase with number of subwarps
Execution time increases with number of subwarps
Performance degrades as number of subwarp increase
Can attacker still recover the AES key?
Notes: Better transition going into FSS attack

## Slide 55: FSS against FSS attack
Attacker can figure out the number of subwarps
Notes: Why FSS attack?

## Slide 56: FSS against FSS attack
Attacker can figure out the number of subwarps
Attacker can calculate per subwarp accesses
Correct guess

## Slide 57: FSS against FSS attack
Attack possible when the attacker can figure out number of subwarps!
  Coalescing still deterministic
Targets the deterministic nature of the coalescing mechanism
  Fixed number of subwarps
  Fixed sizes of subwarp
  Deterministic mapping of the thread elements to subwarps
RCoal to mitigate the correlation timing
attacks

## Slide 58: RCoal: Random Sized Subwarp (RSS)
Size distribution
Normal Distribution
Skewed Distribution
Mean of the distribution is same as FSS
Security and performance similar to FSS
We select RSS with Skewed Distribution
Mean of the distribution is different than FSS
Large subwarp offers better coalescing
Improved security compared to FSS
Improved performance compared to FSS


RCoal to mitigate the correlation timing
attacks
Targets the deterministic nature of the coalescing mechanism
  Fixed number of subwarps
  Fixed sizes of subwarp
  Deterministic mapping of the thread elements to subwarps
RCoal to mitigate the correlation timing
attacks

## Slide 59: RCoal: Random-Threaded Subwarp (RTS)
FSS: number of subwarps = 2
0x00
sid = 0
0x01
sid = 0
0x06
sid = 1
0x07
sid = 1
tid = 0
tid = 1
tid = 2
tid = 3
FSS+RTS: number of subwarps = 2
0x00
0x01
0x06
0x07
tid = 0
tid = 1
tid = 2
tid = 3
Coalescing Unit
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
Coalescing Unit
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x04
0x05
0x06
0x07
sid = 0
sid = 0
sid = 1
sid = 1

## Slide 60: RCoal: Random-Threaded Subwarp (RTS)
RSS: number of subwarps = 2
0x00
sid = 0
0x01
sid = 1
0x06
0x08
tid = 0
tid = 1
tid = 2
tid = 3
RSS+RTS: number of subwarps = 2
0x00
sid = 1
0x01
0x06
sid = 0
0x08
tid = 0
tid = 1
tid = 2
tid = 3
Coalescing Unit
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
Coalescing Unit
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B

## Slide 61: Evaluation Set-up
AES-128
Plaintext with 32 lines
GPGPU-SIM
  15 SMs, 32 threads/warp, one subwarp per coalescing unit (base case)
  GDDR5 Memory with 6 MCs, 16 DRAM-banks, 4 bank-groups/MC
Enhanced Attack Algorithms
  Corresponding Attacks

## Slide 62
Chart: Number of Subwarp
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0
FSS | 0.99846 | 0.99941 | 0.99935 | 0.99771 | 0.94154 | 0
FSS+RTP | 0.99846 | 0.42426 | 0.2569 | 0.080777 | 0.04366 | 0
RSS | 0.99846 | 0.2467 | 0.15489 | 0.13513 | 0.14823 | 0
RSS+RTP | 0.99846 | 0.15216 | 0.095578 | 0.10696 | 0.065268 | 0
Chart: Number of Subwarps
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0
FSS | 1 | 1.0822 | 1.1525 | 1.2189 | 1.2788 | 1.3801
FSS+RTS | 1 | 1.082 | 1.1527 | 1.2198 | 1.2787 | 1.3801
RSS | 1 | 1.0538 | 1.104 | 1.1534 | 1.2455 | 1.3801
RSS+RTS | 1 | 1.0544 | 1.1013 | 1.1547 | 1.2455 | 1.38
Security
(Lower the better)
Execution Time
(Lower the better)
Offers Security/Performance Trade-off
Notes: Mention Rcoal in a BOX

## Slide 63: Conclusions
We proposed RCoal, a set of three novel defense mechanisms
  To mitigate the correlation timing attacks
  Randomizes the memory access coalescing
  Scales with the plaintext size (analysis in paper)
  Theoretical analysis in the paper
RCoal offers a trade-off between security and performance and improves security at a modest performance loss.
Notes: Try to reduce background and introduce rcoal_score

## Slide 64: Future Work
Improving security at lower performance cost
  Adding RCoal-like logic at other parts of the GPU hierarchy
  Software-driven hints to the RCoal-like logic
  Exploring the possibility of new attacks on GPUs
Bandwidth Management Techniques
  Value approximation-based mechanisms
  Unlocking new bandwidth sources in GPUs

## Slide 65: Acknowledgements
More details: http://insight-archlab.github.io/
Gurunath Kadam
(Ph.D. student)
Mohamed Ibrahim (Ph.D. Student)
Fan Luo
(MS student, graduated)
Hongyuan Liu
(Ph.D. student)
Haonan Wang
(Ph.D. student)
Adwait Jog
(Faculty)
Thank you!
Questions?
(Email: adwait@cs.wm.edu)

## Slide 66: Memory Bandwidth Management for Enhanced Throughput and Security in GPUs
Adwait Jog
Assistant Professor of Computer Science
College of William & Mary
http://adwaitjog.github.io/

## Slide 67: RCoal_Score
Security Oriented (a=1, b=1)
Performance Oriented (a=1, b=20)

## Slide 68: Implementation & Overhead

## Slide 69: Evaluation – Case Studies
Chart: 
| Equal | Unequal | Equal | Unequal | WS | FI
 | 1.1968 | 1.0753 | 2.0596 | 1.502
Core Partitioning
PBS enhances WS and FI under both equal and unequal core partitioning scenarios
PBS benefits reduce with unequal partitioning because with different core partitioning each application executes with a different amount of TLP
Core partitioning techniques do not completely solve the interference problem and PBS can provide additional benefits
Notes: Explain Unequal partitioning?
We test PBS under two different core partitioning scenarios: 2:1 and 1:2 partitioning (e.g., in 2:1, the first and the second applications are assigned 20 and 10 cores, respectively) and compare it to our baseline that allocates 15 cores to each application. Figure shows the benefits of PBS over ++bestTLP observed in WS and FI averaged across all our 50 workloads. The bar denoted by Equal represents the average improvement of PBS with equal partitioning, and the bar denoted by Unequal represents the average improvement of PBS with the best performing partitioning scheme among 2:1 and 1:2 (found separately for each workload and then averaged). PBS enhances WS, FI, and HS under both equal and unequal core partitioning scenarios, compared to ++bestTLP. However, the benefits of PBS reduce with unequal partitioning because with different core partitioning each application executes with a different amount of TLP. As we choose the best (among 2:1 and 1:2) core partitioning configuration, the interference is also alleviated because of core partitioning itself in addition to our TLP management schemes. As the design of core partitioning is itself an interesting and non-trivial research problem, we conclude that these techniques still do not completely solve the interference problem and TLP management techniques like PBS can provide additional benefits.

## Slide 70: Evaluation – Case Studies
Chart: 
| Shared | Equal | Shared | Equal | WS | FI
 | 1.1968 | 1.1355 | 2.0596 | 2.2495
Cache Partitioning
PBS improves WS and FI under both Shared and Equal scenarios
Cache partitioning can alleviate the interference at L2
Cache partitioning might be suboptimal (underutilization) when different applications utilize the caches differently
Notes: Explain Shared vs. Equal?
Figure shows the benefits of PBS when the L2 is way-partitioned equally (denoted by Equal) across two applications, and compare it to our baseline where the L2 cache is shared (denoted by Shared). We observe that PBS improves all three metrics (WS, FI, and HS) under both the scenarios. Cache partitioning can alleviate the interference at L2, but it might be suboptimal in scenarios where different applications in the same workload utilize the caches differently. This might lead to a portion of the cache to be not utilized well. On the other hand, PBS changes the cache demand of each application by TLP modulation.

## Slide 71: GPUs – A Closer Look
SIMT Cores
GPU
Memory
L2 cache
Interconnect
…
GPU
Memory
L2 cache
…
Scheduler
SIMT
Lanes
L1 Caches
Threads
W
W
W
W
W
W
Warps
Warp Scheduler

## Slide 72: Working Philosophy
Execution in a SIMT Core
W1
W2
W3
Computation
Waiting for Data from GPU Memory
GPU attempts to hide long memory latency with computation from
other thread warps

## Slide 73: Bandwidth Challenge
GPUs are under-utilized
Chart: 
| SAD | PVC | SSC | BFS | MUM | CFD | KMN | SCP | FWT | IIX | SPMV | JPEG | BFSR | SC | FFT | SD2 | WP | PVR | BP | CON | AES | SD1 | BLK | HS | SLA | DN | LPS | NN | PFN | LYTE | LUD | MM | STO | CP | NQU | CUTP | HW | TPAF | AVG | AVG-T1
 | 0.90269 | 0.86445 | 0.82241 | 0.6484 | 0.71382 | 0.60663 | 0.60584 | 0.43943 | 0.47385 | 0.64708 | 0.64635 | 0.51687 | 0.46336 | 0.4493 | 0.29411 | 0.28971 | 0.47774 | 0.26293 | 0.24463 | 0.16514 | 0.18735 | 0.13915 | 0.15322 | 0.094841 | 0.11532 | 0.1988 | 0.10324 | 0.10689 | 0.048452 | 0.13028 | 0.088976 | 0.041891 | 0.012271 | 0.011149 | 0.00013977 | 0.0053883 | 0.0050535 | 0.0021302 | 0.31524 | 0.54577
55%
GPGPU Applications
Percentage of total execution cycles wasted waiting for the data to come back from memory  Memory Bandwidth is the primary bottleneck

## Slide 74: RCoal Security Enhancement
Except FSS, all defense mechanisms show improvement in the security
RSS based mechanisms generally offer better security
Theoretically 24x to 961x improvement (detailed analysis in paper)
Chart: Number of Subwarps
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0
FSS | 0.99846 | 0.99941 | 0.99935 | 0.99771 | 0.94154 | 0
FSS+RTS | 0.99846 | 0.42426 | 0.2569 | 0.080777 | 0.04366 | 0
RSS | 0.99846 | 0.2467 | 0.15489 | 0.13513 | 0.14823 | 0
RSS+RTS | 0.99846 | 0.15216 | 0.095578 | 0.10696 | 0.065268 | 0
No coalescing,
No correlation

## Slide 75: RCoal Performance
Performance suffers as number of subwarp increase
RSS offers better performance as compared to FSS
RTS does not affect the performance
Chart: Number of Subwarps
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0
FSS | 1 | 1.0822 | 1.1525 | 1.2189 | 1.2788 | 1.3801
FSS+RTS | 1 | 1.082 | 1.1527 | 1.2198 | 1.2787 | 1.3801
RSS | 1 | 1.0538 | 1.104 | 1.1534 | 1.2455 | 1.3801
RSS+RTS | 1 | 1.0544 | 1.1013 | 1.1547 | 1.2455 | 1.38